Compass deviation plug-in for OpenCPN

This plug-in could help you to make a deviaton table for your compass. If it is an electronic compass sending nmea, then an extra nmea sentence with true north heading can be generated.

For determining a deviation on a specific compass course you must, some way or another, compare a true bearing/course with a compass bearing/course.
Finding a true bearing to a point can be done easy by: Drop a waypoint on a mark, and start navigating to this mark. In the pop-up route window you can read the true bearing/course to that point. Another possibility is using the sun. On a given position and time the true bearing of the sun can be calculated. (The calculation is done by the plug-in)

Start with installing the plug-in the usual way. Activate the plug-in by enable in the Options→plug-in menu. Here you can also set the preferences.
Enter your ships name and a compass name. For now make sure that the “Show in toolbar” option is checked.

After ‘OK’ an extra button will show up in the toolbar.

After clicking the toolbar button en empty list with check bearings will pop-up. By clicking ‘Add’ we can enter a deviation checkpoint.
Here we are steaming to a point straight north (000) and reading a compass-course of 002 degrees.

When using the sun as a true bearing point, make sure to use the correct time. On most places the azimuth (bearing) of the sun is changing about 1 degree every 4 minutes.
My compass does have a shadow pin in the middle of the rose, which makes it easy to take a bearing. If your compass does not have one you might use the trick with a string and a weight. Here I use my tea cup as weight. In reality you should make sure that the shadow line of the string runs over the midpoint of the rose.

And add the check to the list. In theory taking 5 check points is enough, however that is theory. In practice try to make 8 checkpoints. Starting at a compass course 000º and from there have one every 45 degrees. Where 000º should be read as “something between 345º and 015º”.
After completing the list, a click on show will bring up the deviation table. Here I used some fake values, and as the points are showing in the graph you can see that the resulting curve is not very exact.
You are supposed to do better.
In case of an electronic compass sending a heading the deviation for the current heading is shown in the toolbar button now. Also if it was checked in the preference a new nmea sentence is sent with the true heading ($--HDT).
It is also possible to print the deviation table to paper.